## Slide 1
How does our sales flow,
and work flow look like?

## Slide 2: Sale Flow
Asset Sale B2C
Direct Website Sales
Ebay, Amazon..
Phone Calls (Yelp, ADs etc.)
Asset Sale B2B
Merchants (Cosco, etc)
Insurance Companies
Government (Veteran Affairs)
Headstone Suppliers
Churches
Cemeteries
Funeral Homes
Online Funeral Suppliers
Phone Calls (Yelp, ADs etc.)
Ebay, Amazon, Paypal
Financing B2C
B2B Commission + Asset Sale
Affiliate Program
Confirm Order Received.
Email customer if need.
Create Preview
Send preview to customer.
Confirm Preview.
Collect Payment.
Start Manufacturing
SALE
Finish Order
& Ship

## Slide 3
Supply Sale
Production of Tooling
Licensing & Franchise B2B
Service Industries (Ex SCI)
Franchise Clients
Funeral Directors
Fiberglass Shops
Headstone Suppliers
Funeral Homes
Asset Sale
B2B Sales
B2C Sales
B2C Financing
B2B Commission Sales
Partial & Full Payments
50% Down payment on Initial Order
50% Balance When Completed
Sale of Materials, Supplies.
YouEulogy.com
Website service platform, complementing features from the headstone product
Advertising
Freemium
Crowd Funding
INCOME

## Slide 4: Sale Prepare Create
1
2
3
4
5
6
7
8
(If it is a printed image, then a additional work step)
Order Stained Glass
Sale of a
Headstone
Buy Supplies, Material
Prepare Molds
(Clean, Wax, Polish)
(Tape paper around
mold for protection)
Prepare the Molds II
Prepare the Material
(Cut the fiberglass mat)
(Breathing Mask, Brush,
Rollers, Containers, Etc.)
Prepare the Supplies
Prepare the Molds III
(Spray PVA, thin film to ease
separation. Cures in 15 min)
The details of the first steps.

## Slide 5
Work Step 1
Spray clear Gelcoat in Mold. wait 15-30 mins until tacky
Work Step 2
Spray Color Gelcoat, or Glitter with Gelcoat, depending color
Work Step 2.2
If Glitter + Clear Gelcoat, then Color Gelgoat as background
Work Step 2B
Laminate the Printed Veil
Work Step 2.2B
Spray Color Gelcoat, which is the background of the Veil
Work Step 3
Lay Skin Coat, which is normally chopped fiberglass
Work Step 4
Lay 2nd Skin Coat, which is a woven fiberglass mat
Work Step 4B
Create Vacuum Bagging, and start the Vacuum
Work Step 5
Tempering: Heat the laminated mold pieces.
Curing Time 1-2 day
Work Step 6
Remove the fiberglass piece(s) from the mold
Work Step 1
Bio-Plant, prepared
Work Step 2
Using our customized shaker, Bio-Plant is combined with a solution
Work Step 3
Bio-Plant goes into a mesh, to drip off excess solution for reclaim
Work Step 4
Bio-Plant wet with solution go into customized shaker
Work Step 5
Combined with granite powder, or other powder type material
Work Step 6
After shaking 5 mins, combined Bio-Plant goes into a mesh to dry
Process is Repeated until QUANTITY reached for next process (avg 1H)
This process gets repeated between wet/dry to build layers, and quantity.
Process is Repeated until LAYERS reached for next process (avg 1H)
Individual Steps Of Parts To Assemble
This step is not present
in Hand-lamination
These are the steps required
for each Headstone &
Nameplate process
Plasmacor © Material Steps
Variation 1
Variation 2
DRY PHASE
WET PHASE

## Slide 6
Work Step 1
Assemble Both Fiberglass Headstone Pieces
Work Step 3
Assemble Stained Glass / Picture With Frame And Insert Into Headstone
Work Step 5
Attach Nameplate
Work Step 6
Seal all gaps with sealant
Work Step 7
Polish Entire Headstone
Work Step 8
Package and Ship
Work Step 2
Fill Headstone With Plasmacor ©
Assembly
Work Step 1
Nameplate Filled with Plasmacor ©
Work Step 2
Back side is sealed with a skin of fiberglass
Work Step 3
Nameplate is removed from the mold and inserted into CNC
Work Step 4
Engraving File uploaded into CNC router, starting machine 2-3h
Work Step 5
Engraved space is filled with color of choice, gold, white, or other
Work Step 6
Entire Nameplate is Polished
Nameplate
Engraving
Process